## Slide 1: Unification of Michele, Jeff, & Brad Ideas
How to formalize the description of messages and transfer procedures By Bradford G. Van Treuren 7/20/2021

## Slide 2: Michele’s RVF Proposal
Data exposes the context of the message. This violates “Separation of Concerns” software rules.
Callback_idf is similar to my “metaname” in my RVFMessage.
There should be no need for optional data if the “transport layer” encapsulates the context.
There should be no difference between Request and Response messages to the “transport layer.”

## Slide 3: Brad’s RVF Proposal
RVFMessage is a “transport layer” wrapper around the underlying protocol message
Adheres to the “Separation of Concerns” rules for OOD
UID contains the identifier of the child (address) sending the message so host knows on which channel the message came from
Metatname specifies the handler context required to process the message
Serialized contains the content of the message being transported
Host Node just routes the RVFMessage to the “transfer module” associated with it
“transfer module” is responsible for deserializing RVFMessage and routing content to appropriate transfer procedure based on metaname
enum RVFType { ERROR = 0; STATUS = 1; REQUEST = 2; RESPONSE = 3; WRAPPER = 4; } message RVFMessage { uint32 UID = 1; RVFType rvf_type = 2; string metaname = 3; bytes serialized = 4; }

## Slide 4: P2654 Influence on P1687.1 Bottom-Up Messaging
P2654 Client Node
P2654 Host Node
P2654 Transport Layer Channel
message RVFMessage { uint32 UID = 1; RVFType rvf_type = 2; string metaname = 3; bytes serialized = 4; }
All DOMAIN messages reside in Serialized as wrapped messages. It does not matter what the context is.
Metaname is used to identify the routing to the appropriate transfer procedure

## Slide 5: P2654 Influence on P1687.1 Bottom-Up Messaging
P2654 Client Node
P2654 Host Node
P2654 Transport Layer Channel
message RVFMessage { uint32 UID = 1; RVFType rvf_type = 2; string metaname = 3; bytes serialized = 4; }
Transfer Module
Creates context specific message from a transfer procedure and packages it in an RVFMessage for channel
Transfer Module
Decodes RVFMessage and calls appropriate transfer procedure associated with metaname or returns an ERROR response
Routes RVFMessage from channel to associated Transfer Module
Routes RVFMessage to channel from associated Transfer Module
Response is just the reverse flow with same RVFMessage type

## Slide 6: P2654 Influence on P1687.1 Top-Down Messaging
P2654 Host Node
P2654 Client Node
P2654 Transport Layer Channel
message RVFCommand {
uint32 IID = 1;
RVFType rvf_type = 2;
string metaname = 3;
bytes serialized = 4;
}
All DOMAIN messages reside in Serialized as wrapped messages. It does not matter what the context is.
Metaname is used to identify the routing to the appropriate transfer procedure

## Slide 7: P2654 Influence on P1687.1 Top-Down Messaging
P2654 Host Node
P2654 Client Node
P2654 Transport Layer Channel
message RVFCommand {
uint32 IID = 1;
RVFType rvf_type = 2;
string metaname = 3;
bytes serialized = 4;
}
Inject Module
Creates context specific message from a transfer procedure and packages it in an RVFCommand for channel
Inject Module
Decodes RVFCommand and calls appropriate transfer procedure associated with metaname or returns an ERROR response
Routes RVFCommand from channel to associated Inject Module
Routes RVFCommand to channel from associated Inject Module
Response is just the reverse flow with same RVFCommand type

## Slide 8: Transfer Module
Transfer Module RVFMessage Handler
metaname
Message1 Handler
Message2 Handler
Message3 Handler
Transfer Procedure

## Slide 9: Additional Slides since 20210720
20210801 Content

## Slide 10: P2654 Node Structure
Insertion from Top
Insertion from Bottom
P2654 Node
Insertion from Top
Insertion from Bottom
P2654 Node
RVFCommand Request
RVFCommand Response
RVFMessage Request
RVFMessage Response
RVFCommand Request
RVFCommand Response
RVFMessage Request
RVFMessage Response
RVFCommand Request
RVFCommand Response
RVFMessage Request
RVFMessage Response
Injection Library
Injection Library
Transform Library
Transform Library

## Slide 11: Top-Down to Bottom-Up Flow
P2654 RVFCommand Sent from Application
Is Node target of RVFCommand
?
Send RVFCommand to next Node
YES
Process RVFCommand with Injection Handler
Create RVFMessage Request to begin Bottom-Up processing for this Node
Send RVFMessage as bottom-up request
Is Node top level controller
?
Transform RVFMessage and pass to next higher level
NO
YES
NO
Transform RVFMessage into HW Controller sequences and apply to HWIF
Create RVFMessage Response from HWIF response and return Response to requester
Is Node command request node
?
Create RVFCommand response and return response to command application
YES
Send RVFMessage to next lowest level
NO