## Slide 1: Theory and Architecture for P2654 and P1687.1
Bradford G. Van Treuren
Draft 11/15/2021

## Slide 2: Key Assumption for Transfer Procedure
Target Grammar
Retargeted Grammar
Transformed Grammar
Behavior
Semantics
Application Perspective
Behavioral Modeling in Software
RetargetedPerspective
Interface Modeling in Software
Interface Perspective
A targeted objective for an instrument may be represented by an interface perspective at the closest accessible access point to the circuit.
Target = Register, Port, Interface, or Message
1
2
3
4
5
6
# | Description
1 | Objective the Application desires to achieve
2 | Describe Target Objectives in terms of the defined language (message tokens) contracted to describe desired Objectives
3 | Transformational algorithm for converting requested Target Message into one or more retargeted Target Objectives required to perform the objective to the Target Interface
4 | Describe retargeted Target Objectives in terms of the defined language (message tokens) contracted to describe the desired Objectives
5 | Translational algorithm for converting retargeted Target Objectives message tokens into instance specific Interface Objectives required to perform the objective to the Node Interface
6 | Describe/Create new Interface Objectives in terms of defined language (message tokens) contracted to describe the desired objectives available at the interface. These become the Target Grammar for the next higher level.

## Slide 3: 1687 to 1687.1 Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Commands with Interface Context
Transformed Values
iWrite Net1, 0x0000507F
iWrite i2cC, 0x02
iWrite i2cD, 0x00
iWrite i2cD, 0x00
iWrite i2cD, 0x50
iWrite i2cD, 0x7F
iWrite i2cC, 0x03
i2cWrite 0x30, 0x02
i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x50
i2cWrite 0x31, 0x7F
i2cWrite 0x30, 0x03
Retargeted Values
Transfer Procedure (Retarget) Phase 1
Transfer Procedure (Transform) Phase 2
Register Context
Interface Context
Target Context
i2cC => 0x30 i2cD => 0x31

## Slide 4: 1687.1 to 2654 Driver Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Code in the Driver Context
i2cWrite 0x30, 0x02
iWrite Xmt, (0x01<<1) & 0xFE
iWrite Ctr, 0x0B
iRead SR, 0x01
iWrite Xmt, 0x30
iWrite Ctl, 0x03
iRead SR, 0x01
write_xmt((0x01<<1) & 0xFE)
write_cntr(0x0B)
while read_status() == 0x01;
write_xmt(0x30)
write_ctrl(0x03)
while read_status() == 0x01;
Retargeted Values
Transformed Values
Transfer Procedure (Retarget) Phase 1
Register Context
Interface Context
Target Context
Xmt => write_xmt() Ctr => write_ctrl()
SR => read_status()
iWrite Xmt, 0x02
iWriteCtl, 0x13
iRead SR, 0x01
iRead SR, 0x02
iWrite Ctl, 0x00
write_xmt(0x02)
write_ctrl(0x13)
while read_status() == 0x01;
if read_status() == 0x02: error;
write_ctrl(0x00)
Transfer Procedure (Transform) Phase 2

## Slide 5: 1687.1 to 2654 Node Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Messages for the Interface Context
i2cWrite 0x30, 0x02
iWrite jtagA, 0x30
iWrite jtagD, 0x02
iWrite jtagC, 0x01
iRead jtagS, 0x01
iWrite jtagC, 0x00
SIR(8, 0x10); SDR(8, 0x30);
SIR(8, 0x11); SDR(8, 0x02);
SIR(8, 0x12); SDR(8, 0x01);
SIR(8, 0x13); SDR(8, 0x00, 0x01, 0x03);
SIR(8, 0x12); SDR(8, 0x00);
Retargeted Values
Transformed Values
Transfer Procedure (Retarget) Phase 1
Transfer Procedure (Transform) Phase 2
Register Context
Interface Context
Target Context
jtagA=> 0x10
jtagD => 0x11
jtagC => 0x12 jtagS=> 0x13

## Slide 6: Transformation Node Model Bottom-Up Processing Flow (IEEE 1687.1 and B-U 2654 ONLY)
TransformNode (Tool Native Language)
Transform Library (C++ Plug-in)
Request Transfer Procedures
Response Transfer Procedures
REQUEST
RESPONSE
REQUEST
RESPONSE
Target Grammar
InterfaceGrammar
CHANGE TO

## Slide 7: Request/Response Flow
Transform Library (C++ Plug-in)
Request Transfer Procedures
Response Transfer Procedures
RESPONSE
REQUEST
REQUEST
XFRM ROUTER
Host Interface
Client Interface
IEEE 2654 Model Node
Instance Data
RESPONSE
TO LOWER LEVEL HIERARCHICAL ELEMENTS
TO HIGHER LEVEL HIERARCHICAL ELEMENTS
handleResponse()
sendRequest()
sendResponse()
handleRequest()
IEEE 2654 Msg Channel
IEEE 2654 Msg Channel
1
2
5
4
3
9
8
7
6
10
# | Description
1 | New Request Arrives from Client
2 | Call handleRequest() of XFRM API
3 | Call XFRM Transfer Proc for Request Type
4 | Create and send new transformed Request(s))
5 | Hand Request to next node to process
# | Description
6 | Response to Request arrives
7 | Call handleResponse() of XFMR API
8 | Call XFRM RevTransfer Proc for Response Type
9 | Create and send new rev transformed Response
10 | Hand Response to Requesting node to process

## Slide 8: Transformation Node Model
System Model
TransformNode (Tool Native Language)
Transform Library (C++ Plug-in)
Request Transfer Procedures
Response Transfer Procedures
REQUEST
RESPONSE
REQUEST
RESPONSE
Node with State Changed (Target Context)
Node Closer to Access Interface (Interface Context)
Target Grammar
InterfaceGrammar
iWrite Net1, 0x0000507F
i2cWrite 0x30, 0x02 i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x50
i2cWrite 0x31, 0x7F
i2cWrite 0x30, 0x03
Request Transfer Procedures convert Target Grammar Commands into one or more Interface Grammar Commands
CHANGE TO
Response Transfer Procedures convert one or more Interface Grammar Responses into one Target Grammar Response for the initiating Target Grammar Request
1
2
3
4
5
6
Target Grammar
Target Grammar
Interface Grammar
Interface Grammar

## Slide 9: 1687/1687.1 Transformation Flow
IEEE 1687 Retargeter
Top 1687 Target ModelPoint
Transform Library
Transfer Procedures
Target Request/ Response
1687.1 Node
Transform Library
Request/ Response
1687.1 DPIC Node
Transform Library

## Slide 10: 1687.1/2654 Transformation Flow
2654 ModelPoint Node
Transform Library
Request/ Response
2654 Node
Transform Library
Request/ Response
1687.1 DPIC Node
Transform Library
2654 Node
Transform Library
2654 System Model
2654 Application
Transfer Procedures

## Slide 11: Transformation/Injection Node Model Top-Down Processing Flow (IEEE 2654 ONLY)
Target Grammar
InterfaceGrammar
Transform Library (C++ Plug-in)
Request Transfer Procedures
Response Transfer Procedures
System Node
2654 Transform
Node
2654 Injection Node (Tool Native Language)
Injection Library (C++ Plug-in)
UPDATE REQUEST
UPDATE RESPONSE
COMMAND
RETURN
REQUEST
RESPONSE
Request Transfer Procedures
Response Transfer Procedures
REQUEST
RESPONSE
REQUEST
RESPONSE
APPLICATION COMMAND BUS

## Slide 12: Command/Return Flow for 2654
# | Description
1 | 2654 Application sends command to a target by reference (path name)
2 | Command is routed to referenced target for processing
3 | Command is decoded into new ordered list of requests for the injection library plug-in
4 | For each request in list, handle request by Injection Library
5 | For each injection request, create target requests for next higher level
6 | For each injection request, create child update requests for each child
7 | For each created target request, call sendRequest() API to send message
8 | For each created update request, call updateRequest() API to send update
9 | Pass target request message to the next level
10 | Pass update request message to next child
11 | As a child, pass update request from host to transform library API updateRequest()
12 | For each child, create update request for child
13 | Pass update request message to next child
14 | Receive response to request from host and call handleResponse() API of Injection Library
15 | Create return message for command handler
16 | For each child, create update response
17 | Pass update response message to next child
18 | As a child, pass update response from host to transform library API updateResponse()
19 | Pass update response message to next child
20 | Process return message and format for return to application
21 | Return return message back to application in response to command call
22 | Return from command call with return data to application
Injection Library (C++ Plug-in)
Transform Library (C++ Plug-in)
UPDATE RESPONSE
UPDATE REQUEST
REQUEST
XFRM ROUTER
Host Interface
Client Interface
IEEE 2654 Model Node
Instance Data
RESPONSE
TO LOWER LEVEL HIERARCHICAL ELEMENTS
TO HIGHER LEVEL HIERARCHICAL ELEMENTS
handleResponse()
sendRequest()
updateResponse()
updateRequest()
IEEE 2654 Msg Channel
IEEE 2654 Msg Channel
1
5
4
9
8
7
6
14
COMMAND
RETURN
Request Transfer Procedures
Response Transfer Procedures
APPLICATION COMMAND BUS
UPDATE REQUEST
IEEE 2654 Msg Channel
UPDATE RESPONSE
COMMAND HANDLER
updateRequest()
updateResponse()
updateResponse()
updateRequest()
For each child
For each child
2
3
handleResponse()
22
10
11
12
13
16
15
17
18
19
20
18
21

## Slide 13
System Model
Transform Library (C++ Plug-in)
System Node
2654 Transform
Node
2654 Injection Node (Tool Native Language)
Injection Library (C++ Plug-in)
UPDATE REQUEST
UPDATE RESPONSE
COMMAND
RETURN
REQUEST
RESPONSE
REQUEST
RESPONSE
APPLICATION COMMAND BUS
Transform Library (C++ Plug-in)
System Node
2654 Transform
Node
2654 Injection Node (Tool Native Language)
Injection Library (C++ Plug-in)
UPDATE REQUEST
UPDATE RESPONSE
COMMAND
RETURN
REQUEST
RESPONSE
REQUEST
RESPONSE
Transform Library (C++ Plug-in)
System Node
2654 Transform
Node
2654 Injection Node (Tool Native Language)
Injection Library (C++ Plug-in)
UPDATE REQUEST
UPDATE RESPONSE
COMMAND
RETURN
REQUEST
RESPONSE
REQUEST
RESPONSE
REQUEST
RESPONSE
2654 Scheduler/Broker
2654 Application
1687.1 EDA Tool
ModelPoint Node
Top-Down /Bottom-Up 1687.1/2654 Transformation Flow

## Slide 14: Dependency Events
Transform Library (C++ Plug-in)
Request Transfer Procedures
Response Transfer Procedures
XFRM ENGINE
System Interface
IEEE 2654 Model Node
Instance Data
set_updateDataValueCallback()
updateDataValueCallback()
1
2
5
4
3
6
# | Description
1 | System model registers updateDataValueCallback() with Transform Library API
2 | Anytime the state of the value of the instance data changes, call updateDataValueCallback() to notify observers dependent on this value of the change
3 | Update system cache of state change
4 | For all observers registered for the dependency data, notify observer of updated value
5 | Each observer manages the affect of the change to the target (e.g., MUX select register changed so call appropriate select() or deselect() methods of the Transform Library API).
6 | Update state of Instance Data to reflect the dependency change
System Model

## Slide 15: Debug Library Capture of Messages
Debug Library (C++ Plug-in)
# | Description
1 | sendResponse() from Transform Library sent from this host to child client interface
2 | updateRequest() coming from a host to this client interface to update the Transform Library
3 | sendRequest() from this Transform Library to the client interface wired to the next level host
4 | handleResponse() from this client interface to the Transform Library or Injection Library depending on type of Request sent
5 | updateRequest() sent from the Transform Library to the host interface wired to children of the node
6 | updateResponse() coming from a host to this client interface to update the Transform Library
7 | updateResponse() sent from the Transform Library to the host interface wired to children of the node
8 | handleRequest() to Transform Library sent from child client interface to this node host interface
9 | sendRequest() from this Injection Library to the client interface wired to the next level host
10 | updateRequest() sent from the Injection Library to the host interface wired to children of the node
11 | updateResponse() sent from the Injection Library to the host interface wired to children of the node
12 | *handleRequest() coming from Command Handler sendRequest() to the Injection Library
13 | *sendResponse() coming from the Injection Library to the Command Handler
Injection Library (C++ Plug-in)
Transform Library (C++ Plug-in)
UPDATE RESPONSE
UPDATE REQUEST
REQUEST
XFRM ROUTER
Host Interface
Client Interface
IEEE 2654 Model Node
Instance Data
RESPONSE
TO LOWER LEVEL HIERARCHICAL ELEMENTS
TO HIGHER LEVEL HIERARCHICAL ELEMENTS
handleResponse()
sendRequest()
updateResponse()
updateRequest()
IEEE 2654 Msg Channel
IEEE 2654 Msg Channel
1
5
4
9
8
7
6
UPDATE REQUEST
IEEE 2654 Msg Channel
UPDATE RESPONSE
updateRequest()
updateResponse()
updateResponse()
updateRequest()
For each child
For each child
3
10
11
RESPONSE
REQUEST
IEEE 2654 Msg Channel
2

## Slide 16: Rules for 1687 Transfer Procedures
A Transfer Procedure is only applied after the 1687 Retargeting phase, applied to the Top Module, is complete for a given objective
Target objectives are only applied as resolved changes following an iApply statement, which has been resolved by the retargeter and not when a statement is executed by the PDL interpreter
Target context commands strictly represent PDL scoped context
Objectives are applied to the target context to which are resolved ICL DataRegisters, ScanInterfaces, or state targets from one or more Top Module elements
Each objective must be completed before another may be applied

## Slide 17: Rules for 1687.1 Transfer Procedures
A Transfer Procedure request shall block execution to wait for a response to be received from the interface indicating the success with data or an error
A Transfer Procedure shall return a response to the target element making the request
If an error occurs during the processing of the request, an error response message shall be returned to the target element making the request
Target context commands strictly represent resolved interface messages
Objectives are applied to the target context to which are resolved Interface Register or state targets
Each objective must be completed before another may be applied
A Transfer Procedure is only applied upon receipt of a request from a target element

## Slide 18: Rules for 2654 Transfer Procedures
A Transfer Procedure request shall block execution to wait for a response to be received from the interface indicating the success with data or an error
A Transfer Procedure shall return a response to the target element making the request
If an error occurs during the processing of the request, an error response message shall be returned to the target element making the request
Target context commands strictly represent resolved interface messages
Objectives are applied to the target context to which are resolved Interface Register or state targets
Each objective must be completed before another may be applied
A Transfer Procedure is only applied upon receipt of a request from a target element

## Slide 19: OLD TO NEW SLIDES

## Slide 20: C/C++ Library Extension Strategy
Leverages protobuffer programming language to support model language and C/C++
Direct call to callback functions from TransformStrategy
Service functions from protoc compile in C or C++ code
SWIG generated or hand crafted to adapt model code to C/C++ callbacks
HOST INTERFACE
TRANSFORMATION ENGINE
CLIENT INTERFACE
TRANSFORM STRATEGY (CALLBACK INTERFACE FAÇADE/
WRAPPER)
handleRequest
handleResponse
sendRequest
sendResponse
getStatus
getError
apply
Extension TransformStrategy
Transform Adapter
SWIG + Callback Library
Node language decoders from message to callback
Transformation Interface
OLD SLIDE

## Slide 21: Request/Response Flow
Transform Library (C++ Plug-in)
Request Transfer Procedures
Response Transfer Procedures
RESPONSE
REQUEST
REQUEST
XFRM ROUTER
Host Interface
Client Interface
IEEE 2654 Model Node
Instance Data
RESPONSE
TO LOWER LEVEL HIERARCHICAL ELEMENTS
TO HIGHER LEVEL HIERARCHICAL ELEMENTS
handleResponse()
sendRequest()
sendResponse()
handleRequest()
IEEE 2654 Msg Channel
IEEE 2654 Msg Channel
1
2
5
4
3
9
8
7
6
10
# | Description
1 | New Request Arrives from Client
2 | Call handleRequest() of XFRM API
3 | Call XFRM Transfer Proc for Request Type
4 | Create and send new transformed Request(s))
5 | Hand Request to next node to process
# | Description
6 | Response to Request arrives
7 | Call handleResponse() of XFMR API
8 | Call XFRM RevTransfer Proc for Response Type
9 | Create and send new rev transformed Response
10 | Hand Response to Requesting node to process

## Slide 22: Stimulus Injection Process
Injection Node sends request for Client Interface context to Injection Strategy
Injection Strategy verifies and forwards message to Client Interface via TransformEngine
Injection Strategy transforms request into updateRequests for children of the Host Interface
Injection Strategy handles response from Client Interface
Injection Strategy passed Client response data to Injection Node
Injection Strategy send an inverse transformed message for the children of Host Interface to update child states
Injection Strategy follows the same implementation/extension mechanism used for Transform Strategy
TestInjectionInterface
Host Interface
Client Interface
Injection Strategy
Transform Engine
Injection Node
handleRequest
sendResponse
sendRequest
handleResponse
updateResponse
updateRequest
apply
Injection Interface
TestInjectionInterface
OLD SLIDE

## Slide 23: Command/Return Flow for 2654
# | Description
1 | 2654 Application sends command to a target by reference (path name)
2 | Command is routed to referenced target for processing
3 | Command is decoded into new ordered list of requests for the injection library plug-in
4 | For each request in list, handle request by Injection Library
5 | For each injection request, create target requests for next higher level
6 | For each injection request, create child update requests for each child
7 | For each created target request, call sendRequest() API to send message
8 | For each created update request, call updateRequest() API to send update
9 | Pass target request message to the next level
10 | Pass update request message to next child
11 | As a child, pass update request from host to transform library API updateRequest()
12 | For each child, create update request for child
13 | Pass update request message to next child
14 | Receive response to request from host and call handleResponse() API of Injection Library
15 | Create return message for command handler
16 | For each child, create update response
17 | Pass update response message to next child
18 | As a child, pass update response from host to transform library API updateResponse()
19 | Pass update response message to next child
20 | Process return message and format for return to application
21 | Return return message back to application in response to command call
22 | Return from command call with return data to application
Injection Library (C++ Plug-in)
Transform Library (C++ Plug-in)
UPDATE RESPONSE
UPDATE REQUEST
REQUEST
XFRM ROUTER
Host Interface
Client Interface
IEEE 2654 Model Node
Instance Data
RESPONSE
TO LOWER LEVEL HIERARCHICAL ELEMENTS
TO HIGHER LEVEL HIERARCHICAL ELEMENTS
handleResponse()
sendRequest()
updateResponse()
updateRequest()
IEEE 2654 Msg Channel
IEEE 2654 Msg Channel
1
5
4
9
8
7
6
14
COMMAND
RETURN
Request Transfer Procedures
Response Transfer Procedures
APPLICATION COMMAND BUS
UPDATE REQUEST
IEEE 2654 Msg Channel
UPDATE RESPONSE
COMMAND HANDLER
updateRequest()
updateResponse()
updateResponse()
updateRequest()
For each child
For each child
2
3
handleResponse()
22
10
11
12
13
16
15
17
18
19
20
18
21

## Slide 24: Debug Recording Strategy
Debug Strategy used to log messages passing through the Model Node
Transform Engine extracts RVF messages from Host/Client Interfaces, Injection Interface, Transform Strategy, and Injection Strategy
Debug Strategy follows the same implementation/extension mechanism used for Transform Strategy
Debug Strategy
Transform Engine
handleRequest
apply
Debug Interface
handleResponse
sendRequest
sendResponse
updateRequest
updateResponse
OLD SLIDE

## Slide 25: Debug Library Capture of Messages
Debug Library (C++ Plug-in)
# | Description
1 | sendResponse() from Transform Library sent from this host to child client interface
2 | updateRequest() coming from a host to this client interface to update the Transform Library
3 | sendRequest() from this Transform Library to the client interface wired to the next level host
4 | handleResponse() from this client interface to the Transform Library or Injection Library depending on type of Request sent
5 | updateRequest() sent from the Transform Library to the host interface wired to children of the node
6 | updateResponse() coming from a host to this client interface to update the Transform Library
7 | updateResponse() sent from the Transform Library to the host interface wired to children of the node
8 | handleRequest() to Transform Library sent from child client interface to this node host interface
9 | sendRequest() from this Injection Library to the client interface wired to the next level host
10 | updateRequest() sent from the Injection Library to the host interface wired to children of the node
11 | updateResponse() sent from the Injection Library to the host interface wired to children of the node
12 | *handleRequest() coming from Command Handler sendRequest() to the Injection Library
13 | *sendResponse() coming from the Injection Library to the Command Handler
Injection Library (C++ Plug-in)
Transform Library (C++ Plug-in)
UPDATE RESPONSE
UPDATE REQUEST
REQUEST
XFRM ROUTER
Host Interface
Client Interface
IEEE 2654 Model Node
Instance Data
RESPONSE
TO LOWER LEVEL HIERARCHICAL ELEMENTS
TO HIGHER LEVEL HIERARCHICAL ELEMENTS
handleResponse()
sendRequest()
updateResponse()
updateRequest()
IEEE 2654 Msg Channel
IEEE 2654 Msg Channel
1
5
4
9
8
7
6
UPDATE REQUEST
IEEE 2654 Msg Channel
UPDATE RESPONSE
updateRequest()
updateResponse()
updateResponse()
updateRequest()
For each child
For each child
3
10
11
RESPONSE
REQUEST
IEEE 2654 Msg Channel
2

## Slide 26: BACKUP SLIDES

## Slide 27: 1687.1/2654 Transformation Flow
2654 Scheduler/Broker
2654 Application
1687.1 EDA Tool
System Model
System Node
System Node
System Node
2654 Node
Transform Library
2654 Node
Transform Library
Request/ Response
2654 ModelPoint Node
Transform Library
2654 Injection Node
Injection Library
2654 Injection Node
Injection Library
2654 Injection Node
Injection Library
Injected Commands

## Slide 28: Key Assumption for Transfer Procedure
Target Grammar
Retargeted Grammar
Transformed Grammar
Behavior
Semantics
Application Perspective
Behavioral Modeling in Software
RetargetedPerspective
Interface Modeling in Software
Interface Perspective
A targeted objective for an instrument may be represented by an interface perspective at the closest accessible access point to the circuit.
Target = Register, Port, or Interface

## Slide 29: 1687 to 1687.1 Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Commands with Interface Context
Transformed Values
iWrite Net1, 0x0000507F
iWrite i2cC, 0x02
iWrite i2cD, 0x00
iWrite i2cD, 0x00
iWrite i2cD, 0x50
iWrite i2cD, 0x7F
iWrite i2cC, 0x03
i2cWrite 0x30, 0x02
i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x50
i2cWrite 0x31, 0x7F
i2cWrite 0x30, 0x03
Retargeted Values
Transfer Procedure (Retarget) Phase 1
Transfer Procedure (Transform) Phase 2
Register Context
Interface Context
Target Context
i2cC => 0x30 i2cD => 0x31

## Slide 30: 1687.1 to 2654 Driver Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Code in the Driver Context
i2cWrite 0x30, 0x02
iWrite Xmt, (0x01<<1) & 0xFE
iWrite Ctr, 0x0B
iRead SR, 0x01
iWrite Xmt, 0x30
iWrite Ctl, 0x03
iRead SR, 0x01
write_xmt((0x01<<1) & 0xFE)
write_cntr(0x0B)
while read_status() == 0x01;
write_xmt(0x30)
write_ctrl(0x03)
while read_status() == 0x01;
Retargeted Values
Transformed Values
Transfer Procedure (Retarget) Phase 1
Register Context
Interface Context
Target Context
Xmt => write_xmt() Ctr => write_ctrl()
SR => read_status()
iWrite Xmt, 0x02
iWriteCtl, 0x13
iRead SR, 0x01
iRead SR, 0x02
iWrite Ctl, 0x00
write_xmt(0x02)
write_ctrl(0x13)
while read_status() == 0x01;
if read_status() == 0x02: error;
write_ctrl(0x00)
Transfer Procedure (Transform) Phase 2

## Slide 31: 1687.1 to 2654 Node Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Messages for the Interface Context
i2cWrite 0x30, 0x02
iWrite jtagA, 0x30
iWrite jtagD, 0x02
iWrite jtagC, 0x01
iRead jtagS, 0x01
iWrite jtagC, 0x00
SIR(8, 0x10); SDR(8, 0x30);
SIR(8, 0x11); SDR(8, 0x02);
SIR(8, 0x12); SDR(8, 0x01);
SIR(8, 0x13); SDR(8, 0x00, 0x01, 0x03);
SIR(8, 0x12); SDR(8, 0x00);
Retargeted Values
Transformed Values
Transfer Procedure (Retarget) Phase 1
Transfer Procedure (Transform) Phase 2
Register Context
Interface Context
Target Context
jtagA=> 0x10
jtagD => 0x11
jtagC => 0x12 jtagS=> 0x13

## Slide 32: Transformation Node Model
System Model
TransformNode (Tool Native Language)
Transform Library (C++ Plug-in)
Request Transfer Procedures
Response Transfer Procedures
REQUEST
RESPONSE
REQUEST
RESPONSE
Node with State Changed (Target Context)
Node Closer to Access Interface (Interface Context)
Target Grammar
InterfaceGrammar
iWrite Net1, 0x0000507F
i2cWrite 0x30, 0x02 i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x50
i2cWrite 0x31, 0x7F
i2cWrite 0x30, 0x03
Request Transfer Procedures convert Target Grammar Commands into one or more Interface Grammar Commands
CHANGE TO
Response Transfer Procedures convert one or more Interface Grammar Responses into one Target Grammar Response for initiating Target Grammar Request
1
2
3
4
5
6

## Slide 33: Rules for 1687 Transfer Procedures
A Transfer Procedure is only applied after the 1687 Retargeting phase, applied to the Top Module, is complete for a given objective
Target objectives are only applied as resolved changes following an iApply statement, which has been resolved by the retargeter and not when a statement is executed by the PDL interpreter
Target context commands strictly represent PDL scoped context
Objectives are applied to the target context to which are resolved ICL DataRegisters, ScanInterfaces, or state targets from one or more Top Module elements
Each objective must be completed before another may be applied

## Slide 34: Rules for 1687.1 Transfer Procedures
A Transfer Procedure request shall block execution to wait for a response to be received from the interface indicating the success with data or an error
A Transfer Procedure shall return a response to the target element making the request
If an error occurs during the processing of the request, an error response message shall be returned to the target element making the request
Target context commands strictly represent resolved interface messages
Objectives are applied to the target context to which are resolved Interface Register or state targets
Each objective must be completed before another may be applied
A Transfer Procedure is only applied upon receipt of a request from a target element

## Slide 35: Rules for 2654 Transfer Procedures
A Transfer Procedure request shall block execution to wait for a response to be received from the interface indicating the success with data or an error
A Transfer Procedure shall return a response to the target element making the request
If an error occurs during the processing of the request, an error response message shall be returned to the target element making the request
Target context commands strictly represent resolved interface messages
Objectives are applied to the target context to which are resolved Interface Register or state targets
Each objective must be completed before another may be applied
A Transfer Procedure is only applied upon receipt of a request from a target element

## Slide 36: 1687/1687.1 Transformation Flow
IEEE 1687 Retargeter
Top 1687 Target ModelPoint
Transform Library
Transfer Procedures
Target Request/ Response
1687.1 Node
Transform Library
Interface Request/ Response
1687.1 DPIC Node
Transform Library

## Slide 37: 1687/1687.1 Transformation Flow
IEEE 1687 Retargeter
Top 1687 Target ModelPoint
Transform Library
Transfer Procedures
Target Request/ Response
1687.1 Node
Transform Library
Interface Request/ Response
1687.1 DPIC Node
Transform Library

## Slide 38: 1687.1/2654 Transformation Flow
2654 ModelPoint Node
Transform Library
Transfer Procedures
Interface Request/ Response
2654 Node
Transform Library
Interface Request/ Response
1687.1 DPIC Node
Transform Library
2654 Node
Transform Library
2654 System Model
2654 Application

## Slide 39: 1687.1/2654 Transformation Flow
2654 ModelPoint Node
Transform Library
Interface Request/ Response
2654 Node
Transform Library
Interface Request/ Response
1687.1 DPIC Node
Transform Library
2654 Node
Transform Library
2654 System Model
2654 Application
Transfer Procedures

## Slide 40: 1687.1/2654 Transformation Flow
2654 ModelPoint Node
Transform Library
Transfer Procedures
2654 Node
Transform Library
Interface Request/ Response
2654 Node
Transform Library
2654 System Model
2654 Application
2654 ModelPoint Node
Transform Library
Transfer Procedures
2654 Node
Transform Library
Interface Request/ Response
2654 Node
Transform Library
2654 System Model
2654 Application

## Slide 41: 1687.1/2654 Transformation Flow
2654 Scheduler/Broker
2654 Application
1687.1 EDA Tool
System Model
System Node
System Node
System Node
2654 ModelPoint Node
Transform Library
2654 Node
Transform Library
Interface Request/ Response
2654 Node
Transform Library
2654 Injection Node
Injection Library
2654 Injection Node
Injection Library
2654 Injection Node
Injection Library
Injected Commands

## Slide 42: 1687.1/2654 Transformation Flow
2654 Scheduler/Broker
2654 Application
1687.1 EDA Tool
System Model
System Node
System Node
System Node
2654 Node
Transform Library
2654 Node
Transform Library
Interface Request/ Response
2654 ModelPoint Node
Transform Library
2654 Injection Node
Injection Library
2654 Injection Node
Injection Library
2654 Injection Node
Injection Library
Injected Commands

## Slide 43: Example Board
IEEE 1149.1
SPI
I2C
U1
U2
U3
U6
U4
U8
U7
U5
SCK
SDA
SCLK
MOSI
SS1
MISO
SS2
TDI
TDO
U9

## Slide 44: Example Board Model
JTAG CONTROLLER
I2C CONTROLLER
I2C BUS
U9
JTAG CHAIN
U1
U2
U3
U6
U4
U5
U7
U8
SPI BUS
I2C BUS
BOARD

## Slide 45: System Example 1
U1
U2
U3
U6
U4
U8
U7
U5
SCK
SDA
SCLK
MOSI
SS1
MISO
SS2
TDI
TDO
U9
U1
U2
U3
U6
U4
U8
U7
U5
SCK
SDA
SCLK
MOSI
SS1
MISO
SS2
TDI
TDO
U9
U1
U2
U3
U6
U4
U8
U7
U5
SCK
SDA
SCLK
MOSI
SS1
MISO
SS2
TDI
TDO
U9
U1
U2
U3
U6
U4
U8
U7
U5
SCK
SDA
SCLK
MOSI
SS1
MISO
SS2
TDI
TDO
U9
U1
U2
U3
U6
U4
U8
U7
U5
SCK
SDA
SCLK
MOSI
SS1
MISO
SS2
TDI
TDO
U9
U1
U2
U3
U6
U4
U8
U7
U5
SCK
SDA
SCLK
MOSI
SS1
MISO
SS2
TDI
TDO
U9
U1
U2
U3
U6
U4
U8
U7
U5
SCK
SDA
SCLK
MOSI
SS1
MISO
SS2
TDI
TDO
U9

## Slide 46: System Example 2
System
Sub-system1
Sub-system1
Sub-system1
USB 3.2
IEEE 802.3
RS-232

## Slide 47: System Example 3, 4, 5
Test Controller
Digital Signal Source1
Analog Signal Source1
Sample Capture/Analyzer Device1
Multimeter
GPIO
Unit Under Test (or loopback)
System Example #5
System Example #4
System Example #3

## Slide 48
RESPONSE
REQUEST
REQUEST
Transform Library
XFRM ROUTER
Host Interface
Client Interface
P2654 Model Node
Instance Data
RESPONSE
Request Transfer Procedures
Response Transfer Procedures
TO LOWER LEVEL HIERARCHICAL ELEMENTS
TO HIGHER LEVEL HIERARCHICAL ELEMENTS
handleResponse()
sendRequest()
sendResponse()
handleRequest()

## Slide 49
RESPONSE
REQUEST
REQUEST
Transform Library
XFRM ROUTER
Host Interface
Client Interface
Instance Data
RESPONSE
Request Transfer Procedures
Response Transfer Procedures
TO LOWER LEVEL HIERARCHICAL ELEMENTS
TO HIGHER LEVEL HIERARCHICAL ELEMENTS

## Slide 50
MBIST4
MBIST2
MBIST3
BYP
Thermometer + Comparator
IP_3
1687 I/F
SIB2
SIB1
WIR
reg
LED
SIB3
WDRmux
WIR mux
SELWIR
MBIST5
mux
IP_2
1687 I/F
SIB2
SIB1
PowerSupplyMonitor
NoiseMaker
SI2
SI1
MBIST1
Functional _Instruments
…
…
Functional _Instruments
DI1

## Slide 51: Example Board
IEEE 1149.1
SPI
I2C
U1
U2
U3
U7
TDI
TDO
TDI2
TDI1
TDO1
TDO2
U4
U5
U6
TDI3
TDO3