## Slide 1: Key Assumption for Transfer Procedure
Bradford G. Van Treuren Presented to P1687.1 WG on 2 Nov 2021

## Slide 2: Permission is granted to use by IEEE as per copyright policy stated in Working Group Meeting
Reference IEEE copyright policy slides shown during every meeting

## Slide 3: Key Assumption for Transfer Procedure
Target Grammar
Retargeted Grammar
Transformed Grammar
Behavior
Semantics
Application Perspective
Behavioral Modeling in Software
RetargetedPerspective
Interface Modeling in Software
Interface Perspective
A targeted objective for an instrument may be represented by an interface perspective at the closest accessible access point to the circuit.
Target = Register, Port, or Interface

## Slide 4: 1687 to 1687.1 Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Commands with Interface Context
Transformed Values
iWrite Net1, 0x0000507F
iWrite i2cC, 0x02
iWrite i2cD, 0x00
iWrite i2cD, 0x00
iWrite i2cD, 0x50
iWrite i2cD, 0x7F
iWrite i2cC, 0x03
i2cWrite 0x30, 0x02
i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x00
i2cWrite 0x31, 0x50
i2cWrite 0x31, 0x7F
i2cWrite 0x30, 0x03
Retargeted Values
Transfer Procedure (Retarget) Phase 1
Transfer Procedure (Transform) Phase 2
Register Context
Interface Context
Target Context
i2cC => 0x30 i2cD => 0x31

## Slide 5: 1687.1 to 2654 Driver Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Code in the Driver Context
i2cWrite 0x30, 0x02
iWrite Xmt, (0x01<<1) & 0xFE
iWrite Ctr, 0x0B
iRead SR, 0x01
iWrite Xmt, 0x30
iWrite Ctl, 0x03
iRead SR, 0x01
write_xmt((0x01<<1) & 0xFE)
write_cntr(0x0B)
while read_status() == 0x01;
write_xmt(0x30)
write_ctrl(0x03)
while read_status() == 0x01;
Retargeted Values
Transformed Values
Transfer Procedure (Retarget) Phase 1
Register Context
Interface Context
Target Context
Xmt => write_xmt() Ctr => write_ctrl()
SR => read_status()
iWrite Xmt, 0x02
iWriteCtl, 0x13
iRead SR, 0x01
iRead SR, 0x02
iWrite Ctl, 0x00
write_xmt(0x02)
write_ctrl(0x13)
while read_status() == 0x01;
if read_status() == 0x02: error;
write_ctrl(0x00)
Transfer Procedure (Transform) Phase 2

## Slide 6: 1687.1 to 2654 Node Transformation Process
INPUT: Target Context
PHASE 1: Retarget target context into interface register context
PHASE 2: Transform interface register context into interface context grammar
OUTPUT: Messages for the Interface Context
i2cWrite 0x30, 0x02
iWrite jtagA, 0x30
iWrite jtagD, 0x02
iWrite jtagC, 0x01
iRead jtagS, 0x01
iWrite jtagC, 0x00
SIR(8, 0x10); SDR(8, 0x30);
SIR(8, 0x11); SDR(8, 0x02);
SIR(8, 0x12); SDR(8, 0x01);
SIR(8, 0x13); SDR(8, 0x00, 0x01, 0x03);
SIR(8, 0x12); SDR(8, 0x00);
Retargeted Values
Transformed Values
Transfer Procedure (Retarget) Phase 1
Transfer Procedure (Transform) Phase 2
Register Context
Interface Context
Target Context
jtagA=> 0x10
jtagD => 0x11
jtagC => 0x12 jtagS=> 0x13